Light Curtain Troubleshooting Guide

- Go to “Frequently Asked Questions” to find your manual and connection diagrams.

- Alignment – If your light curtain has a test input on the sender, verify that it is connected to 24vdc.  You should align the light curtain from both the sender to the receiver, and the receiver to the sender.

- Error code 8 or L2 – This is an EDM (external device monitoring) fault. if you are using the EDM wire on the receiver, verify you have it enabled in your configuration.  If you are not using the EDM wire in the receiver, verify that it is disabled in your configuration.

- Other error codes – consult your light curtain manual.